Parade Captains Meeting Information

Contact Information

R. B. Powell, Nittany Mt. Trail Rides, Inc.  Cell phone:  814-880-5100.

Light Problems, call Scott Barbara  814-321-7781 after 5:00 PM

Accessories for the float wagons.  The parade committee will hand out a safety chain with two screw links and an orange triangle after this meeting.  Nittany Mt. Trail Rides will give out with each wagon a light kit in a bag with two tail lights, six drywall screws, wire with connecting plug, six zip ties to secure wires, a bolt with two standard nuts or one locking nut, and an instruction sheet.

Hitching the wagon to the vehicle.   If you are using a ball hitch insert remove the hitch ball.   Slide the wagon tongue over the flat plate, line up the holes and

put a bolt down through the hole in the bumper or the flat plate of the insert.    Use two nuts on the bolt and tighten the last one on against the first one to jam them tight to secure the bolt.  If you have a locking nut, only one is needed.

Safety Chains

The chain must be looped around the front axle and frame of the wagon and secured with a screw link, grab hook, or closed link of some type.  It is then looped around the wagon tongue and then secured to the tow vehicle at the bumper supports, the safety chain holes in the hitch, the frame of the hitch, or the frame of the vehicle. Use the screw links to make the loops at the end.

Tail Light installation.

Each set of lights will have two tail lights, a specific one for left and right. Look at the markings on the lights and the boards.  Metal lights are fastened to the bed pieces.  They are the heavy planks that run the length of the wagons.

They are to be screwed to the back of the wagon so that the lights are visible at back of the wagon but not protruding beyond the sides.  Three screws are included for each light’s support board.  Two screws are adequate to fasten them.  Run the wires from the lights neatly along the frame of the wagons to the front securing them with zip ties.  Run the wires over the front axle and along the tongue to the light connection on the vehicle.  Leave a little slack to allow for turning.  Use the appropriate adapter or wiring harness if the vehicle does not have a plug.  We will furnish a harness extension if you let us know of the need when we deliver the wagon.   Check the lights with the towing vehicle before decorating the float.  All light kits have been tested.

These wagons are important pieces of equipment for the farmers who lease them to you.  They are worth over $2500 each.  Do not do anything that will leave any changes in the wagon.  You may lengthen it, but do not remove any parts.  If a board is bad or defective, you may replace it.

Secure the wagons and guard the float before the parade to prevent sabotage.

Leave the lights on the wagons, and we will remove them at recycling.  Bring your wagons to recycling Sunday afternoon.